## Slide 1
Six Sigma Quality Improvement
Reduction of Manufacturing Defects in Wooden Toy Production
Chandan Wooden Toys Pvt. Ltd.
DEFINE
MEASURE
ANALYZE
IMPROVE
CONTROL
Team Members : Jatin Kumar Rajput , Riya Gupta , Dev Bhatia , Kaushal Goyal
1/8

## Slide 2
1. Define — Problem, Goal & Scope
What are we trying to improve, and what is included in the project?
Speaker: Member 1
Baseline defect rate
5.44%
593 / 10,909
Project target
≤ 2.50%
Maintain production volume
CTQ
Defect-free toy
Carving + finish + assembly
Baseline period
28 days
Daily production & defects
BUSINESS PROBLEM
• 593 defective toys were recorded during the 28-day baseline.
• 5.44% is the starting defect rate.
• Goal: reduce the overall defect rate toward ≤2.50%.
SCOPE
• IN: carving/shaping, paint/finish, joint/assembly, inspection, defect recording and rework/rejection.
• OUT: marketing, pricing, distribution and customer service.
• Stakeholders: production supervisor, quality inspector, operators and operations manager.
Key idea: Define makes the problem measurable and keeps the project focused.
2/8

## Slide 3
2. Process & Data Collection
SIPOC shows the process; the 28-day dataset provides the evidence.
Speaker: Member 2
SUPPLIERS
Wood / paint / tools
INPUTS
Materials / instructions
PROCESS
Receive → Carve → Paint → Assemble → Inspect
OUTPUTS
Finished / accepted / rejected
CUSTOMERS
End customer / retail / quality
DEFECT CATEGORIES
Carving / Shaping
138
Shape, carving or dimension defects
Paint / Finish
277
Largest defect category
Joint / Assembly
178
Positioning / joining defects
The dataset tracks toys produced, total defectives, each defect category, daily defect rate and daily yield.
3/8

## Slide 4
3. Measure — Baseline Performance & Stability
How large is the problem, and does the process behave consistently?
Speaker: Member 2
Production
10,909
toys
Defective
593
toys
Defect rate
5.44%
baseline
Yield
94.56%
good output
DPMO
18,120
approx.
P-Chart finding
3 special-cause points
Days 8, 15 and 21
These days fall outside the expected 3
limits and should be investigated.
4/8
Chart: Control Chart
Pi=yi/ni | 0.032877 | 0.060847 | 0.048295 | 0.068354 | 0.040541 | 0.058537 | 0.036313 | 0.093827 | 0.052356 | 0.072864 | 0.03866 | 0.055825 | 0.043836 | 0.069378 | 0.015 | 0.058667 | 0.04902 | 0.035912 | 0.06506 | 0.046154 | 0.090909 | 0.034946 | 0.057214 | 0.048913 | 0.063107 | 0.041237 | 0.051852 | 0.077889
P bar | 0.054359 | 0.054359 | 0.054359 | 0.054359 | 0.054359 | 0.054359 | 0.054359 | 0.054359 | 0.054359 | 0.054359 | 0.054359 | 0.054359 | 0.054359 | 0.054359 | 0.054359 | 0.054359 | 0.054359 | 0.054359 | 0.054359 | 0.054359 | 0.054359 | 0.054359 | 0.054359 | 0.054359 | 0.054359 | 0.054359 | 0.054359 | 0.054359
LCL | 0.018757 | 0.019374 | 0.018105 | 0.020136 | 0.018998 | 0.020767 | 0.018411 | 0.020561 | 0.019558 | 0.020265 | 0.019828 | 0.020849 | 0.018757 | 0.02109 | 0.02035 | 0.019235 | 0.020685 | 0.01861 | 0.02097 | 0.019917 | 0.02109 | 0.019093 | 0.020435 | 0.018902 | 0.020849 | 0.019828 | 0.020561 | 0.020265
UCL | 0.089961 | 0.089343 | 0.090612 | 0.088582 | 0.089719 | 0.08795 | 0.090307 | 0.088157 | 0.089159 | 0.088453 | 0.088889 | 0.087869 | 0.089961 | 0.087627 | 0.088367 | 0.089483 | 0.088032 | 0.090108 | 0.087747 | 0.088801 | 0.087627 | 0.089624 | 0.088283 | 0.089815 | 0.087869 | 0.088889 | 0.088157 | 0.088453

## Slide 5
4. Analyze — Pareto: Where Is the Problem?
Focus first on the defect category contributing the most.
Speaker: Member 3
#1 Priority
Paint / Finish
277 defects = 46.7%
#2 Priority
Joint / Assembly
178 defects = 30.0%
#3 Priority
Carving / Shaping
138 defects = 23.3%
Pareto tells us WHERE to focus; it does not prove WHY.
5/8
Chart: 
Defect Count | 277 | 178 | 138
Cumulative % | 0.46712 | 0.76728 | 1

## Slide 6
v
5. Analyze — Root Cause Analysis
Fishbone + 5 Why narrow the investigation toward process-control variation.
Speaker: Member 3
5 WHY: Finish varies → application/drying varies → method depends on judgement → parameters are not consistently documented/checked
Leading root-cause hypothesis: insufficient standard work + visual controls. Validate during the pilot.
6/8
MACHINE
Tool wear
Paint equipment variation
Maintenance / calibration
MATERIAL
Wood condition / moisture
Paint viscosity / batch
Adhesive consistency
MEASUREMENT
Defect classification
Inspection consistency
Recording accuracy
HIGH MANUFACTURING DEFECT RATE
MAN
Operator technique
Training / experience
Fatigue / handover
METHOD
Paint quantity / coats
Drying time
Assembly sequence
First-piece approval
ENVIRONMENT
Dust / cleanliness
Temperature / humidity
Workstation conditions

## Slide 7
6. Improve & Control — Solutions, FMEA and Reaction Plan
Turn the analysis into practical actions and a system for sustaining gains.
Speaker: Member 4
IMPROVEMENT ACTIONS
1
Paint/Finish SOP + visual standard
2
Minimum drying time + first-piece approval
3
Assembly fixture / poka-yoke
4
Daily tool check + replacement trigger
5
Common defect-definition guide
FMEA PRIORITY
Failure mode
S×O×D
RPN
Priority
Incorrect paint application
8×7×5
280
High
Insufficient drying
7×6×6
252
High
Wrong joint positioning
8×5×5
200
Medium
CONTROL
• Daily: defect rate + category trends; P-chart/KPI.
• Every batch: 100% first-piece approval; hold if missing.
• Weekly: SOP audit; target ≥95%.
• Green = continue; Yellow = review; Red = investigate, correct and verify.
7/8

## Slide 8
7. Conclusion — The Six Sigma Story
What the project found and what happens next.
5.44%
Baseline defect rate
46.7%
Paint/Finish share
280
Highest FMEA RPN
≤2.50%
Project target
KEY TAKEAWAYS
• 593 defects were found in 10,909 toys during the baseline.
• Paint/Finish is the first improvement priority, followed by Joint/Assembly.
• The leading root-cause hypothesis is variation in standard work and process controls.
• The proposed solution is to standardize work, catch problems earlier and monitor the process daily.
Next step: run the pilot and compare post-improvement data with the 5.44% baseline. Do not claim ≤2.50% until data confirms it.
Speaker: Member 4
8/8